## Slide 1
Nov. 13, 2019
D. Ratner
SLAC National Accelerator Laboratory
Machine Learning for an XFEL accelerator

## Slide 2
Machine learning at SLAC
Online Control of Facilities
Offline
data analysis
Megapixel detector
Intensity map from multiple pulses
Interpretation of structure / dynamics
Accelerator control
Accelerator diagnostics
X-ray diffraction image
Cryo-
EM
LCLS-II
Critical Need:
Big facilities
Big data rate
New machine learning initiative focusing on ML for facilities
ML applications:
Computer vision
Neural networks
Bayesian optimization
Gaussian processes
Anomaly/breakout detection
Reinforcement-learning
Predictive control
Edge-ML
People involved:
ML experts
Software engineers
Domain scientists
Students
Visitors
Stanford/SV

## Slide 3
Outline
Online optimization of accelerators
Surrogate modeling
Data analysis: ghost imaging

## Slide 4
Optimization
Online tuning:
XFELs are instabilities  very sensitive to initial conditions
In total 500 hours/year on single task of quad tuning
Ocelot
Automate (e.g. simplex)

## Slide 5: Optimization: Bayesian optimization
Acquisition point
Acquisition
function
Ground truth
Posterior
Model-based optimization
Gradient optimizer
Advantage 1: Balance “exploitation vs. exploration”
 Find global maximum
Bayesian optimizer
M. McIntire

## Slide 6: Optimization: Bayesian optimization
Instance based learning  similarity function
x1
x2
x3
x*
Advantage 2: Existence of model enables use of physics, archived data
Model-based optimization
Measured
Modeled
FEL vs quads (i.e. strong focusing)
Quad 1
Quad 1
Quad 2
Joe Duris

## Slide 7: Optimization: Bayesian optimization
Advantage 2: Existence of model enables use of physics, archived data
Model-based optimization
ρ = 0.7
ρ = 0
Groundtruth
Model,
no correlation
Model,
w/ correlation
Joe Duris
Instance based learning  similarity function

## Slide 8: Optimization: Bayesian optimization
Joe Duris
Model-based optimization
Example 2: tuning quadrupoles from pure noise
Example 1: Fast tuneup in high dimensions
Upshot:  Faster tuning (factor of 4 vs. simplex)
 More robust tuning (e.g. tune from noise)
Bayesian Optimization of a FEL, Duris et al., arXiv:1909.05963
4 parameters
12 parameters

## Slide 9: Optimization: Bayesian optimization
Adi Hanuka
Model-based optimization
Example 3: Tune-up at SSRL
Easy to extend to new facilities
Upshot:  Faster tuning (factor of 4 vs. simplex)
 More robust tuning (e.g. tune from noise)
Tuning beam size at SSRL

## Slide 10: Optimization: Prognostics
Anomaly/Breakout detection
Failure prediction
Root-cause analysis
Fault recovery
Time
FEL Pulse
Energy
Cathode QE
zoom
Example: Recover from fault that caused ~5 hours of downtime
D. Sanzone

## Slide 11
Outline
Online optimization of accelerators
Surrogate modeling
Data analysis: ghost imaging

## Slide 12: Surrogate Models: Accelerator models
J. Qiang
measurement
simulation
High fidelity physics simulations are remarkable:
…but also slow. (e.g. hours on NERSC)
How can we best support design of a new machine?
LCLS-II simulations, Y. Ding
LCLS microbunching instability

## Slide 13: Surrogate Models: Accelerator models
Auralee Edelen

## Slide 14: Surrogate Models: Collective effects
Auralee Edelen
Notes: Genesis simulations provide users very accurate prediction of X-ray pulses for preparing for shifts and testing analysis methods. However, each simulation takes ~1000s of CPU-seconds. For users who require large numbers of examples, e.g.crystallography or statistical methods like ghost imaging, Genesis is too slow.
Generative adversarial networks (GANs) use two networks: the “discriminator” tries to identify if an example is real (i.e. Genesis), or fake (i.e. the “generator”). The generator tries to fool the discriminator. As the two networks fight, the generator makes more and more realistic examples. Images at right show a generated fake XTCAV image (upper right) and the associated X-ray profile (lower right, green). The blue curve is what the old XTCAV algorithm would have estimated from the fake example, showing that the generated example is reasonable.

## Slide 15: Surrogate Models: Update from data
Auralee Edelen

## Slide 16: Surrogate Models: FEL simulations
Genesis:
~1000 cpu-sec
GAN (neural net):
~0.001 gpu-sec
Generative adversarial network (GAN)
Modeling collective effects from shot noise
X. Ren
Benefit: Provide users with rapid pulse generator
(1 million times faster than Genesis)
Notes: Genesis simulations provide users very accurate prediction of X-ray pulses for preparing for shifts and testing analysis methods. However, each simulation takes ~1000s of CPU-seconds. For users who require large numbers of examples, e.g.crystallography or statistical methods like ghost imaging, Genesis is too slow.
Generative adversarial networks (GANs) use two networks: the “discriminator” tries to identify if an example is real (i.e. Genesis), or fake (i.e. the “generator”). The generator tries to fool the discriminator. As the two networks fight, the generator makes more and more realistic examples. Images at right show a generated fake XTCAV image (upper right) and the associated X-ray profile (lower right, green). The blue curve is what the old XTCAV algorithm would have estimated from the fake example, showing that the generated example is reasonable.

## Slide 17
Outline
Online optimization of accelerators
Surrogate modeling
Data analysis: ghost imaging

## Slide 18: Data Analysis: Ghost imaging / Single-pixel camera
Riddle: How can I take a picture with a spectrometer?
Answer: Have a friend with a flashlight
So what is ghost imaging anyway?

## Slide 19: Data Analysis: Ghost imaging / Single-pixel camera
Target, x
b = [ 5037,
4783,
4891, … ]
Reconstructed Target, x*
Bucket measures total transmission
Radiation, a
Classic GI formalism:
Raster scan
Ghost imaging
“Fellgett’s” (or Multiplex) advantage
TJ Lane, D Ratner, arXiv preprint arXiv:1907.12178, 2019

## Slide 20: Data Analysis: Compressive sensing
Compressive sensing concept:
Why record 660k points if only 39k needed?
Wikimedia
Trick: Use “prior” information to reconstruct the sample
e.g. Sky is uniform blue  minimize “total variation” of image

## Slide 21: Data Analysis: Ghost imaging / Single-pixel camera
Classic GI formalism:
Compressive sensing formalism:
=
b
x
Matrix of all patterns
a
Target, x
b = [ 5037,
4783,
4891, … ]
Reconstructed Target, x*
Bucket measures total transmission
Radiation, a
TJ Lane, D Ratner, arXiv preprint arXiv:1907.12178, 2019
raster
GI
Measurement is easier than control!
Solve with e.g. ADMM, Plug & Play, etc.

## Slide 22: Data Analysis: cathode ghost imaging
Simulated
Ground truth
Reconstruction
photocathode quantum efficiency
DMD
Cathode laser
Cathode
target
Ground truth
Reconstruction
Natural laser jitter
Siqi Li
Day 1
Day 3
K. Kabra, et al., arXiv preprint arXiv:1910.11926, 2019
Real data
(no ground truth)

## Slide 23: Data Analysis: Pump-probe ghost imaging
Ghost imaging in the time domain
Pump X-ray
Time
Sample, CO
System (CO) evolves after absorbing X-ray, changing electron energies
Array of buckets (B)
Incident radiation (P)
target
A. Picon
Delay (fsec)
Electron energy (eV)
Target (x)
Probe X-ray
e-
t
“Pump-probe” scan of delay, t
D Ratner et al., Physical Review X, 9, (1), 011045

## Slide 24: Data Analysis: Pump-probe ghost imaging
Ghost Imaging Summary
Felgett’s/Multiplex Advantage: Boost signal to noise ratio
Compressive sensing: converge to solution faster using priors
‘Measurement is easier than control’: Use what nature gives you for easier, faster, higher resolution measurements
Sample dose reduction is NOT an advantage
Felgett’s advantage does NOT work for Poisson detectors

## Slide 25: Data Analysis: Pulse reconstruction
Maxwell, Timothy J., et al. International Society for Optics and Photonics, 2014.
Spectrum
How can we measure femtosecond X-rays?
Power (W)
Time (fs)
After lasing
Before lasing
e- energy (g)
e- energy (g)
Electron phase space

## Slide 26: Data Analysis: Pulse reconstruction
Computer vision
Stanford CS231n
D. Mendez
Aphex34 https://commons.wikimedia.org/w/index.php?curid=45679374

## Slide 27: Data Analysis: Pulse reconstruction
Ground truth
XTCAV
time
energy
Old algorithm
ML model
Power (W)
Time (fs)
Before lasing
e- energy (g)
After lasing
e- energy (g)
X. Ren
XTCAV Analysis

## Slide 28: Data Analysis: Pulse reconstruction
Power (W)
Time (fs)
Before lasing
e- energy (g)
After lasing
e- energy (g)
X. Ren
Slippage dominates in saturation
XTCAV Analysis
Ground truth
Old algorithm
ML model

## Slide 29: Data Analysis: Pulse reconstruction
Full beam reconstruction
Measure amplitude of power/spectrum: can I recover phase?
Measure Power
Measure Spectral power
Guess
Field
F(t),F(w)
Measure Power
Measure Spectral power
Hidden layers
Output
Input
Guess
Field
F(t),F(w)
…
106-109 times
Pulse #1
Pulse #n
Only solve once!

## Slide 30: Data Analysis: Pulse reconstruction
Xiao Zhang
Full beam reconstruction
Measure amplitude of power/spectrum: can I recover phase?
Measure Power
Measure Spectral power
Hidden layers
Output
Input
Guess
Field
F(t),F(w)
Only solve once!
Input power
Power ground truth
Power prediction
Power
Phase
Phase GT
Phase prediction
Input Power

## Slide 31: Data Analysis: Pulse reconstruction
Xiao Zhang
Full beam reconstruction
Measure amplitude of power/spectrum: can I recover phase?
Measure Power
Measure Spectral power
Hidden layers
Output
Input
Guess
Field
F(t),F(w)
Only solve once!
Input power
Power ground truth
Power prediction
Power
Phase
Phase ground truth
Phase prediction
Input Power

## Slide 32
Department of Energy Round Table:
ML for control of X-ray, Neutron, and Nano-facilities
Four panels:
Online control
Data Acquisition
Modeling/Simulations
Multimodal analysis

## Slide 33: Conclusion
ML Mantra:
Orders of magnitude/new science,
That which can be automated, should be automated.
Ge Wang
(Stanford)
That which cannot be meaningfully automated should not be automated.

## Slide 34: Conclusion
Thanks to collaborators
E. Cropp, J. Cryan, J. Duris, A. Edelen, A. Hanuka, K. Kabra, A. Kennedy, T. J. Lane, S. Li, A. Lutman, G. Marcus, P. Musumeci, X. Ren, G. Stupakov, G. Wetzstein, X. Zhang
Many other topics for ML and accelerators:
virtual diagnostics, anomaly/breakout detection, in-the-loop experimental control, physics for/from ML, UQ …
https://ml.slac.stanford.edu/
We’re hiring for ML at SLAC!

## Slide 35: Surrogate Models: FEL simulations
Training Set
Genesis Simulation
GAN
Feed Training Data
Data Augmentation
CNN
The generative adversarial network (GAN) generates labeled images
 Augment training for CNN or other data-hungry algorithms
Unlabeled data
Labeled Training Set
X. Ren
Convolutional neural network (CNN) recovers X-ray power with smaller errors than current state-of-art
Training Pipeline
Experiment
Notes: Genesis simulations provide users very accurate prediction of X-ray pulses for preparing for shifts and testing analysis methods. However, each simulation takes ~1000s of CPU-seconds. For users who require large numbers of examples, e.g.crystallography or statistical methods like ghost imaging, Genesis is too slow.
Generative adversarial networks (GANs) use two networks: the “discriminator” tries to identify if an example is real (i.e. Genesis), or fake (i.e. the “generator”). The generator tries to fool the discriminator. As the two networks fight, the generator makes more and more realistic examples. Images at right show a generated fake XTCAV image (upper right) and the associated X-ray profile (lower right, green). The blue curve is what the old XTCAV algorithm would have estimated from the fake example, showing that the generated example is reasonable.

## Slide 36: Data Analysis: Pump-probe ghost imaging
Spectral ghost imaging
Note that we never actually need power, only autocorrelation!
From Wiener-Khinchin theorem:
HXSSS
A. Picon
Delay (fsec)
Electron energy (eV)
Electron bins
X-ray spectra
Time dynamics!
Spectral power:

## Slide 37: Data Analysis: Pump-probe ghost imaging
Spectral ghost imaging
Note that we never actually need power, only autocorrelation!
For Gaussian wave-packets
Pearson correlation coefficient, A(2) and A(1)
Siegert relation:
(limit of infinite pulse, proper normalization)
FEL’s have second relation:
From Wiener-Khinchin theorem:
Spectral power:
0
G. Stupakov

## Slide 38: Data Analysis: Pump-probe ghost imaging
Spectral ghost imaging
Note that we never actually need power, only autocorrelation!
Ground truth
Ap, high res
Ap, low res
Af, low res
Delay
Delay
Delay
Delay
Empirically still works for 1st order autocorrelation
 Two advantages: Spectrometers are cheap, resolution only affects
From Wiener-Khinchin theorem:
Spectral power:

## Slide 39: Gaussian Process Optimizer
Gaussian process: instance based learning method
Covariance function:
observations
new point
prior mean
new point to predict
taken from M. Ebner, GP for Regression

## Slide 40: Gaussian Process Optimizer
Gaussian process: instance based learning method
observations
new point
prior mean
new point to predict
Prediction of new point:
Variance of new point:
Covariance function:
taken from M. Ebner, GP for Regression

## Slide 41: Gaussian Process Optimizer
Gaussian process: instance based learning method
observations
new point
prior mean
new point to predict
Acquisition function:
Covariance function:

## Slide 42: Optimization: Bayesian optimization
Gaussian processes
observations
new point
prior mean
new point to predict
Prediction of new point:
Variance of new point:
Covariance function:
M. Ebner,
GP for Regression
Acquisition function (UCB):