## Slide 1: Design and expected performance of the neutron guide systems at Breazeale Reactor at Penn State University
Márton Markó
Alex Szakál, Kenan Ünülü, Péter Kárpáti

## Slide 2
GOAL
Breazeale Reactor
1MW research reactor
built in 1955
Reconstructed in 2020
Under installation:
Cold source
Guide system

## Slide 3
GOAL OF THE NEUTRON GUIDE SYSTEM
3 + 1 COLD INSTRUMENTS:
PGAA & NDP:
SANS
(V16 from Berlin)
TBD
3 NEUTRON GUIDES
GOAL

## Slide 4
PGAA & NDP:
  White beam
  Thermal equivalent intensity
  ∼ cm sample
  Low bacground: γ, n, and other particles
    Moderate divergence
Sample
Detector
Neutron beam
INSTRUMENTAL NEEDS
Vacuum chamber

## Slide 5
SANS:
  Moderate wavelength resolution (3-20 %)
  Divergence: 0.3o – 1.2 o
  Beam spot: 2-8 cm total width
  0.5 - 2cm sample size
  λmin = 3Å
INSTRUMENTAL NEEDS
TOF mode: choppers
CW mode: velocity selector

## Slide 6
CONSTRAINTS
In-pile section with vacuum jacket
Guide hall
SANS collimator house
PGAA / NDP background
CONSTRAINTS

## Slide 7
Guide Shapes
  GT1: SANS: 4X4cm
  GT2: Middle guide: 2.5 X 10 cm
  GT3: PGAA & NDP: 2.5 X 2.5 cm
Guide cross-sections
DESIGN – GENERAL OVERVIEW
  SANS: straight – bender – straight - focusing
  Middle guide: curved – straight – flight tube
  PGAA & NDP: curved - straight

## Slide 8
  Will be built later
  Designed for high intensity
  70 X 25 mm (h,w)
  Curved guide: 17.5m, m=3
  R = 1120 m
  Straight guide: 7m, m=3
  flux: 9.8e7 n/s/cm2
GT2 middle guide
DESIGN GT2 guide
Phase space: curved guide
Phase space: at the end

## Slide 9
  Will be built later
  Designed for high intensity
  70 X 25 mm (h,w)
  Curved guide: 17.5m, m=3
  R = 1120 m
  Straight guide: 7m, m=3
  flux: 9.8e7 n/s/cm2
GT2 middle guide
Phase space: curved guide
Phase space: at the end
DESIGN GT2 guide

## Slide 10
  25 X 25 mm (h,w)
  Curved guide: 12.5m, m=3
  Straight guide: 3m, m=3
  R = 500 m
  Flight tube: 1.5m
  Itot : 8.3e7 n/s
  Itherm.eq: 2.3e8 n/s
GT3 PGAA & NDP
DESIGN GT3: PGAA / NDP

## Slide 11
  40 X 40 mm (h,w)
  Straight guide: 5m, m=3
  Bender: 4.4 m, 10 ch.
  m=3.5, m=2, R=37m
  Straight guide: 3.5 m, m=1.2
  3 X 2m focusing guide m = 1.5
  flux: 1.7e7 n/s/cm2
GT1 SANS
DESIGN GT1 SANS

## Slide 12
SANS Collimation section
    Sample – detector distance:
7.7m : 0.3o
1.7m : 1.2o
    Straight / focusing guides
    in collimation section
Intensity gain = 1.4
centre shift: 0 whithin error
FWHM (GE} 0.51 cm 0.545 cm
DESIGN GT1 SANS
N. Stüßer,T.Hofmann NIM A 727(2013)84–89

## Slide 13
SANS Collimation section
    Sample – detector distance:
7.7m : 0.3o
1.7m : 1.2o
    Straight / focusing guides
    in collimation section
Intensity gain = 1.4
centre shift: 0 whithin error
FWHM (GE} 0.51 cm 0.545 cm
DESIGN GT1 SANS

## Slide 14
Chopper system:
1. ch: 0m 11.1o
2. ch: 0.05m 22.2o
3. ch: 0.6m 26.32o
4. ch: 5.1m 60o
Detector: 18.3m - 23.4m
DESIGN GT1 SANS

## Slide 15
 | A (HR) | B (HI) | C (HWB)
Wavelength band [Å] | 5.8 | 5 | 7.4
Intensity [1e4 n/cm/s] | 3.7 | 5.2 | 4
f [1/s] | 20.1 | 29.4 | 36.7
 | A (HR) | B (HI) | C (HWB)
Pulse shaping | CH #1 | CH #3 | CH # 2 double speed
Frame overlap | CH #3 | CH #2 | CH #3
Wavelength Band | CH #4 | CH #4 | CH #4
3 (+∞) Chopper modes
DESIGN GT1 SANS

## Slide 16
 | A (HR) | B (HI) | C (HWB)
Wavelength band [Å] | 5.8 | 5 | 7.4
Intensity [1e4 n/cm/s] | 3.7 | 5.2 | 4
f [1/s] | 20.1 | 29.4 | 36.7
 | A (HR) | B (HI) | C (HWB)
Pulse shaping | CH #1 | CH #3 | CH # 2 double speed
Frame overlap | CH #3 | CH #2 | CH #3
Wavelength Band | CH #4 | CH #4 | CH #4
3 (+∞) Chopper modes
DESIGN GT1 SANS

## Slide 17
Calculation ws simulation:
Real FWHM
GE FWHM (from variance) simulation
GE FWHM (from variance) from calculation
Analitical / MC calcuations

## Slide 18
Velocity selector
For continuous mode
with relaxed resolution
8% resolution from 6Å
18% at 2Å
(40 % at 1.2Å)
Possible resolution / wawelength map for different tilt angle
DESIGN GT1 SANS

## Slide 19
Thanks to
Daniel Clemens (HZB)
László Szentmiklósi (CER, BNC)
László Almásy(CER, BNC)
Kenan Ünülü (PSU)
Alex Szakál (CER, BNC)
Péter Kárpáti (CER, BNC)
MIRROTRON company

## Slide 20
Thank you for your attention!