## Slide 1: The new versions 3.5 and 4.0 of the vitess simulation package
K. Lieutenant
F. Beule
J. Voigt
P. Zakalek
Z. Ma
6th International Workshop Neutron Delivery Systems, NDS 2023
Grenoble, 11 - 14 Oct 2022

## Slide 2: Aim and Features of Vitess
Aims
  Simulation of neutron scattering instruments
  Virtual neutron scattering experiments
Options
  GUI
  Modular structure
  Polarisation included
  Absolute flux values calculated
  …

## Slide 3: VITESS Team
Current developer team (FZJ, since 2019)
Klaus Lieutenant Fabian Beule Paul Zakalek Jörg Voigt
Contributing authors
First developers (1999 – 2005) ESS Upgrade phase (2011 – 2014)
Geza Zsigmond Dietmar Wechsler Friedrich Streffer Michael Fromme Sergey Manoshin Daniil Nekrassov Carolin Zendler
  Andreas Houben Mirko Boin Jennifer Schulz Phillip Bentley Dickon Champion

## Slide 4: Realization by Monte Carlo Simulations
free parameters:
wavelength λ
initial position x,y
initial direction vhor/v, vvert/v
dir. after monochr. θm, φm
scattering direction θs, φs
Basic Idea: Random choice of parameters instead of scanning through parameter space

## Slide 5: Modules representing Components in vitess 3.4
Sources
reactor
SPSS
LPSS
lens
detector
res. Drabkin
simple coll.
Choppers
Fermi str.
disc
Fermi curv.
bender
guide
Samples
elast. isotr.
SANS
powder
inelastic
reflectom.
sngl.crys.
S(Q)
Modules f. Polaris.
SM-polar.
³He-polar.
coil flipper
grad. flipper
SM ensemb
Soller coll.
Space + Windows
multiple windows
window/ beamstop
space
grid
rot. field
prec. field
slit
pol. mirror
Collimator
environm.
quadr.field
radial coll.
vel.select
ellipt. mirror
Optics / Transport
beamstop
5
ideal guide
NXS
Monochr.
old
new
capture flux
Various

## Slide 6: Modules for Data Evaluation
Evaluate
elast
elast_sans
Monitor 1
Time
Wavelen
y-/z-pos
div-y/-z
visualize
frame
writeout
MonPol 1
Time
Wavelen
y-/z-pos
div_y/-z
MonPol 2
y-pos z-pos
Monitor 2
y-pos z-pos
div-y div-z
TOF λ
z div-z
λ div_y/-z
y div-y
spin_reset
capt_flux
Trajector.
Geometr.
elast2
inelast
runtime
k-y k-z
rad div-rad
Mon1D
MonBrill
Mon2D

## Slide 7: Concept of VITESS
source
module 2
module n
I(par)
graphical user interface
monitor
param. file
instrument.inf
param.file
parameters
parameters
parameters
parameters
sim_data
log_file

## Slide 8: New features in Vitess 3.5 and 4.0
General
  Reflectivity curves for supermirror coating updated 3.5
  Code tided up 3.5
  Safe connection between GUI and kernel 3.5
  Blow up of width and height in the visualization 3.5 or 4.0
  New visualization tool (GR from FZ Jülich) 3.5 or 4.0
  New GUI (Qt) 4.0
Instrument simulations for HBS
  Source module for CANS 3.5
  Rotating monochromator 3.5
  Improved import and export of neutron trajectories 3.5
Virtual experiments at MLZ
  Improved reflectometer sample 3.5
  Monitor update during run 3.5
  Instrument saved as YAML file 4.0
  Avoiding parameters from file 4.0

## Slide 9: GUI of VITESS

## Slide 10: Updating of monitor output
Simulation split into a number of bunches, e.g. 10 x 1 Mio trajectories
All monitor outputs are updated after each bunch
Estimated intensity in the monitor channels roughly constant by considering the fraction of the simulated trajectories
Update triggered by special ‘trajectory’

## Slide 11: guide

## Slide 12: Coating described by m-value
Chart: m=3.0
Company 2 | 0.994 | 1.02 | 1.01 | 0.987 | 1.017 | 0.986 | 1.012 | 1.01 | 1.006 | 0.992 | 0.987 | 1.01 | 0.994 | 0.998 | 0.99 | 0.979 | 0.983 | 1.005 | 0.984 | 0.998 | 0.972 | 0.968 | 0.977 | 0.977 | 0.977 | 0.972 | 0.965 | 0.951 | 0.942 | 0.955 | 0.948 | 0.962 | 0.942 | 0.944 | 0.93 | 0.955 | 0.929 | 0.916 | 0.935 | 0.934 | 0.912 | 0.929 | 0.936 | 0.917 | 0.925 | 0.926 | 0.92 | 0.93 | 0.926 | 0.888 | 0.796 | 0.511 | 0.208 | 0.071 | 0.046 | 0.036 | 0.025 | 0.021 | 0.018
Chart: m=5.0
R0 = 0.995
W = 0.00157 Å-1
m = mnom+0.14
Rcut = Min(R0,1.096 – 0.0758 m)
Rcut
R0

## Slide 13: Sm ensemble

## Slide 14: rotating monochromator

## Slide 15: Reading and writing of Mcnp data
VITESSMcStas
Simulation of instrument part M using VITESS or McStas
Simulation of instrument part N using VITESS or McStas
VITESSMcStas
monitor
guide
writeout
read_in
Binary and Ascii files can be read and written now
Data evaluation
VITESSMcStas
Simulation of the TMR unit using MCNP or any other program
MCPL WSSA
Simulation of shielding, radiation background, …
using MCNP etc
MCPL
MCPL
Determination of source characteristics

## Slide 16: Example: Reading Mcnp data of HBS simulation
VITESSMcStas
Ta
Top view

## Slide 17: Visualization completed

## Slide 18: Blow-up
Same trajectories visualized by a blow-up factor of 100 perpendicular to the beam direction.
Neutron scattering instruments are often very long, especially on long pulse sources. The length can be a factor of 1000 larger than width and height. This makes a visualization in 1:1:1 scale quite useless
A blow-up factor for width and height enables trajectory visualization
50 trajectories inside a double elliptic neuton guide of 2x50 m length and 100 mm maximal width, visualized in 1:1:1 scale

## Slide 19: Visualization by GR graphics
Instrument simulations for HBS

## Slide 20: Visualization by GR graphics
Instrument simulations for HBS

## Slide 21: GUI of VITESS 4.0 using Qt

## Slide 22: Virtual experiments at mlz (example maria)
Requirements
  Describe MARIA with all details in a VITESS simulation
  Enable all movements and settings
  Enable continuous monitor output
  Include simulation in NICOS
  Web application
Goals
  Training of the instrument operation for new users
  Assessment of proper instrument settings for a sample of interest
  Estimation of required beamtime
  Replacement of real experiments in case of reactor failure

## Slide 23: yaml files to store instruments and define gui
Module ‘velselect’
Part of a SANS instrument

## Slide 24: Less Parameters from file in vitess 4
Parameters in files are difficult to control by NICOS or in numerical optimization

## Slide 25: Status 3.5 and 4.0
VITESS 3.5
  Programming finished
  Function test finished
  2 problem left with instrument visualization
  Blow-up has to be tested still
  Planned Release: July 2023
VITESS 4.0
  GUI completed
  Kernel completed
  Code to ensure unique component name has to be implemented
  Updating monitor files during run has to be improved
  Intensive testing necessary
  Planned Release: in September 2023

## Slide 26: Modules representing Components in vitess 3.4
Sources
reactor
SPSS
LPSS
lens
detector
res. Drabkin
simple coll.
Choppers
Fermi str.
disc
Fermi curv.
bender
guide
Samples
elast. isotr.
SANS
powder
inelastic
reflectom.
sngl.crys.
S(Q)
Modules f. Polaris.
SM-polar.
³He-polar.
coil flipper
grad. flipper
SM ensemb
Soller coll.
Space + Windows
multiple windows
window/ beamstop
space
grid
rot. field
prec. field
slit
pol. mirror
Collimator
environm.
quadr.field
radial coll.
vel.select
ellipt. mirror
Optics / Transport
beamstop
26
ideal guide
NXS
Monochr.
old
new
capture flux
Various

## Slide 27: Modules representing Components in vitess 3.5
Sources
reactor
SPSS
LPSS
lens
detector
res. Drabkin
simple coll.
Choppers
Fermi str.
disc
Fermi curv.
bender
guide
Samples
elast. isotr.
SANS
powder
inelastic
reflectom.
sngl.crys.
S(Q)
Modules f. Polaris.
SM-polar.
³He-polar.
coil flipper
grad. flipper
SM ensemb
Soller coll.
Space + Windows
multiple windows
window/ beamstop
space
grid
rot. field
prec. field
slit
pol. mirror
Collimator
environm.
quadr.field
radial coll.
vel.select
ellipt. mirror
Optics / Transport
beamstop
27
ideal guide
NXS
Monochr.
old
new
capture flux
filter 2D
Various

## Slide 28: Modules representing Components in vitess 4.0
Sources
simple src
CW source
pulsed src
Monochr.
new
simple coll.
Choppers
Fermi str.
disc
Fermi curv.
guide
Samples
elast. isotr.
SANS
powder
inelastic
reflectom.
sngl.crys.
S(Q)
Modules f. Polaris.
SM ensemb
Space + Windows
window
space
slit
Collimator
environm.
radial coll.
vel.select
Optics / Transport
beamstop
28
ESS source
ISIS source
detector
filter 2D
Various
SM-polar.

## Slide 29: Modules representing Components in vitess 4.1
Sources
simple src
CW source
pulsed src
Monochr.
new
lens
cylindr. field
simple coll.
Choppers
Fermi str.
disc
Fermi curv.
bender
guide
Samples
elast. isotr.
SANS
powder
inelastic
reflectom.
sngl.crys.
S(Q)
Modules f. Polaris.
SM-polar.
³He-polar.
coil flipper
grad. flipper
SM ensemb
virtual coll.
Space + Windows
multiple windows
window
space
grid
rot. field
prec. field
slit
pol. mirror
Collimator
environm.
quadr. field
radial coll.
vel.select
ellipt. mirror
Optics / Transport
beamstop
29
ideal guide
NXS
simpl. guide
twist. guide
ESS source
ISIS source
detector
capture flux
filter 2D
Various
old
res. Drabkin
prism

## Slide 30: Tiding up
Vsn 3.4
Vsn 3.5

## Slide 31: Tiding up
Vsn 3.5

## Slide 32: Single crystal diffractometer
Applications
  Single crystals of proteins and other biological molecules (Laue diffraction)
Concept and Requirements
  TOF diffractometer using whole pulse
  Medium resolution Δλ/λ < 3%
  High flux in 1 x 1 mm²
  Low background
  Variable divergence and ‘clean’ distribution
Choices
  TS 1, LH2 moderator
  Medium frequency (96 Hz, 250 µs pulse)
  20.4 m total length
  SELENE optics (no direct line of sight)
  Large detector coverage (3° - 170° ?)
Characteristics
  Bandwidth: 2 Å, standard: 2 – 4 Å
  d-range : 1.0 – 76 Å
  λ-resolution: 1.3% - 2.4%
  Estimated flux at sample: 4·107 n/(cm²s)
Staff
  Design: Tobias Schrader
  Simulations: Zhanwen Ma
TOF-Laue diagram for myoglobin
Ma et al., publication in preparation

## Slide 33
Thank you for your attention
Union Module: combining several components in 1 module to enable
  Multiple scattering
  Parallel components
  …..
1000 minor improvements
Transition to C++
Plans for the future

## Slide 34: The Pipe Command and Export in version 3
Instrument can be exported from GUI to
  Batch file
  Perl script
  Python script
  Shell script
  Tcl script
  Grid shell sript
This can be edited to
  Calculate parameters
  Run a series
  Run an optimization

## Slide 35: Structure of Functions and Classes
Sample
SANS
Init
Matrix
Intersection
Source
Powder
Src_modchar
General
Softabort
Message
main C functions of a module
application specific C functions
general (complex) C functions
basic C functions and classes
mathmatrix
mon2D
mathvector
class
functions
35

## Slide 36: Gui – kernel connection
Vsn 3.5

## Slide 37: Gui – kernel connection
GUI
Kernel

## Slide 38: Less Parameters from file in vitess 4
So they are reduced to the minimum
Current kernel can handle both ways of input

## Slide 39: Hbs source In vitess and mcstas
Example: parameters of the thermal source at the 1st target station (96 Hz)
McStas component: Source_pulsed

## Slide 40: Disordered materials diffractometer
Application
  PDF measurements on liquids, amorphous materials and nano-particles
Concept and Requirements
  TOF diffractometer using whole pulse
  Medium resolution by long instrument
  Short min. wavelength for high Q-values
Choices
  TS 3, D2O moderator
  Frequency (96 Hz, 167 µs neutron pulse)
  85 m length
  Detector range: 10° - 140°
Characteristics
  Bandwidth: 0.69 Å, standard 0.1 – 0.79 Å
  Resolution: 1.3% - 7.8%
  Q-range : 1.9 – 118 Å-1
  Estimated flux at sample: 107 n/(cm²s)
Staff
  Design: Mikhail Feygenson
  Simulations: Zhanwen Ma
Strong flux gain by short distance between moderator and guide
Z. Ma et al., Nucl. Instrum. Methods Phys. Res. A 1008 (2021) 165479.

## Slide 41: Status of vitess 3.5
Sources
reactor
SPSS
LPSS
lens
detector
res. Drabkin
simple coll.
Choppers
Fermi str.
disc
Fermi curv.
bender
guide
Samples
elast. isotr.
SANS
powder
inelastic
reflectom.
sngl.crys.
S(Q)
Modules f. Polaris.
SM-polar.
³He-polar.
coil flipper
grad. flipper
SM ensemb
Soller coll.
Space + Windows
multiple windows
window/ beamstop
space
grid
rot. field
prec. field
slit
pol. mirror
Collimator
environm.
quadr.field
radial coll.
vel.select
ellipt. mirror
Optics / Transport
beamstop
41
ideal guide
NXS
Monochr.
old
new
capture flux
filter 2D
Various
complete
vis. test miss.
vis. missing
bug
not yet tested

## Slide 42: Parameter set transferred
ID
criterion ‘ray tracing’
‘colour’
Time of flight t [ms]
wavelength λ [Å]
intensity p [n/s]
location of neutron x [cm]
location of neutron y [cm]
location of neutron z [cm]
flight direction vx/|v| = cos α
flight direction vy/|v| = cos β
flight direction vz/|v| = cos γ
Spin Sx
Spin Sy
Spin Sz
Right-handed system
x: along the beamline y: to the left z: (vertically) up
y
x
z
view from moderator towards sample
Data set of each trajectory

## Slide 43: Hbs source In vitess & Mcstas
VITESS Source and Moderator Parameters
HBS Source in McStas

## Slide 44: Instruments presented in the TDR
Single crystal diffractometer
Disordered materials diffractometer
Thermal powder diffractometer
Engineering diffractometer
Diffuse elastic scattering
Polarized diffuse neutron spectrometer
6 Diffractometers
Specular reflectometer (using SELENE optics)
Off-specular reflectometer
Hi Throughput SANS
SANS with GISANS option
SANS with VSANS option
(LoQ diffractometer)
6 Large Scale Structure Instruments
Cold imaging instrument
Refractive imaging instrument
Thermal imaging instrument
Epithermal imaging instrument
4 Imaging Instruments
Neutron resonance spin echo instrument
Neutron spin echo spectrometer
Backscattering spectrometer
Cold chopper spectrometer
Thermal chopper spectrometer
X-TOF spectrometer
Inverted Geometry spectrometer
(Vibrational spectrometer)
8 Spectrometers
Prompt gamma neutron activation analysis
TOF prompt gamma neutron activation analysis
Neutron depth profiling
3 Analytics Instruments
The TDR will comprise performance studies of 27 instruments installed on the three target stations.
Based on these results, it will be chosen at a later stage, which instruments will be built in which order.
Simulated using VITESS
Simulated using McStas

## Slide 45: pulse shape and peak brilliance of the hbs
96 Hz 24 Hz
1.6% duty cycle
τproton : 167 µs
τneutron: 252 µs
τproton : 667 µs
τneutron: 665 µs
First target-moderator simulations showed that HBS will have about the same peak brilliance as FRM-2

## Slide 46
Hbs floor PLan
46
TS 1 96 Hz
TS 2 24 Hz
TS 3 96 Hz?

## Slide 47: The hbs performance
Time averaged brilliance of the two moderators