## Slide 1: Investigation of Pancake-like Moderator-Reflector Structure for the High Brilliance Neutron Source (HBS)
Junyang Chen
Forschungszentrum Jülich
12.07.2023

## Slide 2
Background
Need for neutron-scattering facilities :
growing
Some existing reactor-based sources :
decommissioned
High Brilliance Neutron Source (HBS))
Basic paradigm
Produce less but more efficiently
Save cost
HBS layout
Wide application of neutron

## Slide 3
High Brilliance Neutron Source (HBS))
Main features
Proton energy : 70 MeV
Proton beam power : 100 kW
Three target station : 24 Hz, 96 Hz, 96 Hz
10-12 instruments for each target stations
Optimal time structure and energy structure : fulfill the needs of each individual instrument
Key component to “more efficiently”
Moderator-Reflector
1)Moderator : decrease neutron energy
2)Reflector : reflecting escaping neutron
Neutron transfer system

## Slide 4
Low energy
Proton beam (high energy)
Target
Small target
Small Neutron cloud with high density
Single tube is ideal case
HBS Moderator-reflector : Confinement and Extraction
Proton beam (low energy)
Target
Extraction channel inside cloud with specific moderator
Optimal energy with high brilliance

## Slide 5
Extraction:
Specific moderator in the channel
Diameter of channel should be larger (6 cm)
Mean free path of thermal neutron
in water : 0.5-1 cm
Multiple channels
Dilute neutron cloud
Multiple channel Extraction
Losing moderator material

## Slide 6
Confinement in water
H2O
D2O
Be
Graphite
Thermal neutron cloud distribution
Thermal moderator: water
High scattering cross section
High energy loss per collision
Fill in the space to confine neutron cloud
Pb
Pb
Pb
Pb

## Slide 7
Low dimensional moderator
Cold moderator material : paraH2 (20k)
Low dimensional moderator
Suitable dimension to avoid decreasing brilliance transfer
L. Zanini, et al., JAEA-Conf 20-15-002, 2014
L. Zanini, ESS Seminar, 2023

## Slide 8
neutron
Premoderator
Cold moderator
Moderator /Reflector
neutron
Without gap inside moderator
High brilliance
Pancake structure

## Slide 9
Pb
parahydrogen
water
target
Point detector
1m
Circular slit; Boron (thickness 0.01cm, density 200g/cm3)
Tally for brightness

## Slide 10
Shortage of Pancake structure
Pancake
parahydrogen
water
Single tube
parahydrogen
parahydrogen
Triangle channel
Pancake problem
Center paraH2 :
dilute thermal neutron cloud
Only cold neutron
Top layer

## Slide 11
Water
Parahydrogen (20K)
neutron
Transverse
section
Water inside the parahydrogen can increase the cold neutron flux by 1.33
Thickness
Without water
Water inside parahydrogen pancake

## Slide 12
Absorption effect of water for cold neutron
Tally point
Cold neutron absorbed by center water
Exponential decay for increasing thickness of center water
Absorption cross section of H

## Slide 13
1
2
3
4
Multiple extraction for one dimension
Water
Parahydrogen (20K)
Circular parahydrogen is in the center
Different parahydrogen channels are separated by water
Different parahydrogen channels correspond to different instruments

## Slide 14
Water surrounding pancake
1. Single Pancake
2. Water surrounding: moderating and reflecting escaping neutron
3. Water inside: increasing cold neutron flux
4. Water filling: increasing feeding thermal neutron
5 Gap : vacuum space

## Slide 15
Different effect of thermal and cold moderator
Water : 1) confine thermal feeding neutron cloud
2) provide thermal neutron to instruments
Large and fill in the space
Small and close to center
Thermal neutron feeding
Thermal neutron feeding
Thermal neutron feeding
Thermal neutron feeding
Cold moderator
Thermal moderator

## Slide 16
12 extraction channels
8 channels for cold neutron
4 channels for thermal neutron
Thermal neutron extraction
Pb

## Slide 17
Thermal neutron flux distribution
Cold neutron flux distribution
Cold neutron brightness : at least 24 % increased (compared with triangle channel)
Thermal neutron brightness : at least 20 % increased (compared with triangle channel)
Provide neutron up to 12 instruments
Result

## Slide 18
Outlook
Bi-spectral extraction
Influence of engineering problem for neutronics
1) Container between cold moderator and water
2) Neutronic influence of cooling circuit
Compatibility with neutron delivery system

## Slide 19
Thanks to HBS Team
J. Baggemann
Th. Brückel
T. Cronert (†)
Q. Ding
P.-E. Doege
T. Gutberlet
J. Li
K. Lieutenant
Z. Ma
E. Mauerhofer
N. Ophoven
U. Rücker
N. Schmidt
A. Schwab
J. Voigt
P. Zakalek
- Core group: design, verification,
instrumentation
ZEA-1:
Y. Bessler
R. Hanslik
R. Achten
F. Löchte
M. Strothmann
- Engineering
IKP-4:
O. Felden
R. Gebel
A. Lehrach
M. Rimmler
R. Similon
- Nuclear physics
INM-5:
B. Neumaier
- Radio isotopes
S. Böhm
J.P. Dabruck
R. Nabbi
- Nuclear simul.
C. Lange
T. Langnickel
Ch.Haberstroh
M. Klaus
S. Eisenhut
- AKR-2, liquid H2
H. Podlech
O. Meusel
- Accelerator
W. Barth
- Accelerator
/ HIM