## Slide 1: Improvements of the knowledge of actinides on the HPRL for nuclear energy
Carole Chatel1, 2, 3, 4, 5, 6
Jonathan Wilson7, Philippe Dessagne1, Greg Henning1, Maëlle Kerveno1, Olivier Bouland†5, Gilles Noguère5 and Maria Diakaki5, Ludovic Mathieu6, Mourad Aïche6, Peter Möller8
1Université de Strasbourg, CNRS, IPHC/DRS UMR 7178, 23 Rue du Loess, F-67037 Strasbourg, France
2Technische Universität Darmstadt, Fachbereich Physik, Institut für Kernphysik, Schlossgartenstrasse 9, 64289, Darmstadt, Germany
3GSI Helmholtzzentrum für Schwerionenforschung, 64291, Darmstadt, Germany
4Helmholtz Forschungsakademie Hessen für FAIR (HFHF)
5CEA, CAD, DES, IRESNE, DER, SPRC, Physics Studies Laboratory, F-13108 Saint-Paul-lez-Durance, France
6Univ. Bordeaux, CNRS, CENBG, UMR 5797, F-33170 Gradignan, France
7CNRS, IJClab Orsay, bât 100, 15 rue G. Clemenceau, 91406 Orsay Cedex, France
8P. Moller Scientific Computing and Graphics, 1888 Kalakaua Ave, Suite 3104, Honolulu, HI 96815

## Slide 2: Nuclear reactions on the HPRL
Neutronics codes for fast neutron reactors or large core reactors:
Use evaluated nuclear data files as input based on:
  experimental data
  state of the art of theoretical modeling
Two examples:
238U(n,n’):
  Codes have uncertainties mainly due to 238U(n, n’)
    XS uncertainties target: 2-3% (HPRL); currently overestimated ~10% in the 2–5 MeV energy region (source: A. Santamarina, et al., Nucl. Data Sheet 118, (2014))
242Pu(n,f)
  Candidate for the fission chamber to monitor the RJH reactor (CEA Cadarache)
  Disregarded in previous evaluation because of the fertile character
Source : M. Kerveno et al. ND2022 - presentation
2

## Slide 3: 238U(n,n’)

## Slide 4: Why studying the 238U level scheme
Large uncertainties in the current modeling are related to the knowledge of the decay scheme: poorly known BR and an incomplete information of the discrete states above 1.3 MeV
Uncertainties in level schemes induce uncertainties in inelastic cross sections (e.g. 10% on BR can have an impact of around 4% on (n, n’g) XS. Sensitivity analysis made by Greg Henning with the TALYS code, M. Kerveno et al. PRC 104, 044605, 2021))
Source : M. Kerveno et al. ND2022 - presentation
 Need to improve the level scheme knowledge to infer the total (n, n’) XS
4
Prompt g-ray spectroscopy is a powerful method which provides a lot of cross sections:
  (n, xng)
  Level production
  Total (n, xn)
Notes: IN ENSDF : average uncertainties on BR : 8%

## Slide 5: n-Ball experiments
5
Realized in 2018 and 2022
ALTO accelerator
Neutrons beam LICORNE (Lithium Inverse Cinematiques ORsay NEutron source) mono-energetic and pulsed (400 ns) focused forward
Comprised 2 rings of 12 Clover HPGe

## Slide 6: 238U level scheme - obtained results
6
118 levels identified
  Including 60 already listed in ENSDF
  Including 92 found with both n-Ball data
268 g transitions identified
  Including 110 already listed in ENSDF
  Including 187 found with both n-Ball data
43 new g transitions depopulating levels already known in ENSDF
58 new levels (not known in ENSDF)
115 new g transitions (de)populating these new levels

## Slide 7: 238U level scheme - obtained results
Branching ratios calculated
Jp deduced by
  completing bands
  Selection rules allowing maximum E2 transitions
Completness verified
7

## Slide 8: 242Pu(n,f)

## Slide 9: 242Pu(n,f) - Nuclear structure background
  Resolved Resonance Range (RRR)
  Neutron continuum
  thermal slope
  Unresolved Resonance Range (URR)
1 eV
1 keV
10 keV
Neutron Energy (eV)
Fission cross section (b)
9
Notes: Donner les énergies des régions

## Slide 10
  fission
Sn(243Pu) = 5,031 MeV
Sn(242Pu) = 6,309 MeV
243Pu well
242Pu well
241Pu well
Low lying levels
n + 242Pu
(n,f) : first chance fission
(n,n’f) : second chance fission
Neutrons
242Pu well
Low lying levels
Sn(242Pu) = 6,309 MeV
10
Nuclear structure background

## Slide 11
11
Prior state of the art:
Multi level Breit-Wigner (MLBW) approximation : no more mandatory those days
Switch to the RM approximation
Cumulative of fission widths
800
700
RRR: Work with CONRAD (CEA tool)
2 Class-II states identified
Working with a Lorentzian in cumulative

## Slide 12
12
 Reference data: fission cross section measured by Auchampaugh et al.  Hauser-Feshbach (HF) description of fission (TALYS code) combined with Lorentzian penetrability
Still working with a Lorentzian in cumulative Extension of URR from 40 keV to 100 keV
URR: Work with TALYS
68 Class-II states identified

## Slide 13: Deduction of the EII value
Class-II states sequences generated by the ”Quasi Particle Vibrational Rotational Level Density” (QPVRLD) of the AVXSF-LNG code
Comparison of truncated sequences with the cumulative curve and average spacing of the identified Class-II states
Comparison of the sequences with CTM curves
Deduction
13

## Slide 14: AVXSF-LNG: Generation of sequences
14
Sn = 5.034 MeV [RIPL-3]
EII = 1.53 MeV [RIPL-3]
EII = 1.7 ± 0.3 MeV [S. Bjornholm and J.E. Lynn]
Excitation energy:
  Sn – EII = 3.334 MeV
Considering uncertainties + study over 100 keV, Class-II states sequence generated between 3.034 Mev and 3.734 MeV
Creation of 13 partial sequences considering EII between 1.4 and 2.0 MeV by steps of 0.05 MeV
Notes: uses a macro-microscopic combinatory method

## Slide 15: Use of the truncated sequences Comparison with the identified class-II states
15
Average spacing:
Low energies: gathering of Class-I states identified as Class-II states
Higher energies: missing Class-II states (most of them above 40 keV)
Between 0 and 10 keV: 28 states  DII = 0.37 keV
  Comparing with partial sequences:
  possible values of EII: 2.00, 1.90, 1.85, 1.75, 1.70, 1.65 and 1.55 MeV
Between 0 and 20 keV: 28 + 19 = 47 states  DII = 0.43 keV
  Comparing with partial sequences:
  possible values of EII: 1.95, 1.90, 1.85, 1.80, 1.75, 1.70 and 1.65 MeV
2 studies:
between 0 and 10 keV
between 0 and 20 keV
 EII values below 1.55 MeV; 1.60 MeV and 2.00 MeV can be excluded
Notes: Comparison with Weigmann: 0.77 keV and 0.67 keV

## Slide 16: Use of the truncated sequences Comparison with the identified Class-II states
16
Cumulative number of Class-II states:
RMSD calculated for each sequence & shape of the curve compared
Between 0 and 10 keV:
  Comparing with partial sequences:
  Best values of EII: 1.90, 1.95 MeV
  Possible other values: 1.50, 1.55, 1.60, 1.70 and 1.75 MeV
Between 0 and 20 keV:
  Comparing with partial sequences:
  Best value of EII: 1.95 MeV
  Possible other values: 1.70, 1.75, 1.80, 1.85, 1.90 MeV
 EII values of 1.45 MeV and 2.00 MeV can be excluded
 EII values of 1.40 MeV; 1.50; 1.60; 1.65 and 1.85 MeV seems also far away
Notes: Distribution

## Slide 17: Use of the full sequences Comparision with a CTM
: full sequence from 0 to 3.734 MeV simulated by AVXSF-LNG
According to Lynn, Talou and Bouland [PRC97, 2018], properties of the second fission well are closer to those of the first well than to those of the barriers.
T = 0.43258 ± 0.03765 MeV & U0 = -0.70434 ± 0.11634 MeV in the first well [RIPL-3]
T = 0,37291 MeV [TALYS]
17
Notes: Considering En, the energy of the incident neutron and by decoupling N (U ) = N (EII → Sn) + N (Sn → En) and integrating between EII and Sn + En,

## Slide 18
18
Use of the full sequences Comparision with a CTM
1.90 MeV ≤ EII ≤ 1.95 MeV

## Slide 19: Conclusion
238U:
n-Ball & n-Ball2 data have been analysed by g-g coincidence
118 levels identified
  Including 58 not listed in ENSDF
268 g transitions identified
  Including 158 not listed in ENSDF
242Pu:
70 Class-II states have been identified
EII value deduced from identified Class-II states, AVXSF-LNG sequences & CTM
1.90 MeV ≤ EII ≤ 1.95 MeV
19

## Slide 20: Thank you 

## Slide 21: CONTEXT
PWR reactors core : neutron radiation absorptions = Buildup of higher mass actinides
Sub-threshold Eneutron: σf(fissile)>> σf(fertile)
Above the threshold: σf(fissile) ≈ σf(fertile)
Disregarded in previous evaluation because of the fertile character
Monitoring of:
MOx
RJH : Occitane
Fast Reactor
Study of 242Pu fission becomes important
PWR - UOx
21

## Slide 22
  RRR
  URR
  Continuum
  RRR : Observed class I and class II resonances
  Continuum :
242Pu fission cross section (barn)
En (eV)
242Pu fission cross section (barn)
Energy (MeV)
  << 1  RRR
  1  URR
  > 1  Continuum
  Mean spacing when En when En
  URR : Observed unresolved class I resonances and resolved class II resonances
Energy (MeV)
En (eV)
En (eV)
242Pu fission cross section (barn)
Class-II states identified during this PhD compared with: - H. Weigmann, J.A. Wartena, C. Bürkholz, Neutron-induced fission cross section of 242Pu, Nuclear physics A438, 333-353, 1985 - G.F. Auchampaugh, C.D. Bowman, Parameters of the subthreshold fission structure in 242Pu, Physical Review C, Volume 7 number 5, 1972
  Class II resonances partially damped
  Class I resonances fully damped
22
Basics
Notes: Barrières=seuil

## Slide 23
Evaluated files: resonances are not identified by their class in ENDF file
Reconstructing the observed XS  no information on physics
Phenomenological
Class II states: local amplification with a Lorentzian shape
Best way:
By identifying, one knows what is reproduced
23
Experimental observation of class II states

## Slide 24: Fitting the cumulative fission widths
  Based on a Lorentzian approximation:
  ECII the energy of the class-II state ΓCII the width the class-II state σCII the magnitude of the class-II state
Cumulative of fission widths (meV)
En (eV)
Cumulative of fission widths
24

## Slide 25: Fitted fission widths
Energy (eV)
Prior fission widths as a function of energy
Fission widths (eV)
Energy (eV)
Posterior fission widths as a function of energy
Fission widths (eV)
More statistically distributed

## Slide 26: Identification of class II states in urr
Coarse evaluation of the URR fluctuation fission XS in the ENDF file
242Pu fission cross section (mbarn)
Energy (keV)
1 kev
100 kev
10 kev
242Pu fission XS (mbarn)
En (eV)
26

## Slide 27: Identification of class II states in URR
Again: no specification of class II states in the ENDF file
 Reference data: fission cross section measured by Auchampaugh et al.  Hauser-Feshbach (HF) description of fission (TALYS code)
Still working with a Lorentzian in cumulative Extension of URR from 40 keV to 100 keV
 Resolving 68 class-II states in URR
Cumulative of fission XS (b)
En (eV)
27

## Slide 28: Use of the truncated sequences Comparison with the identified Class-II states
Consideration of the channel opening
Assumption:
  s from 0
  p from 7 keV
  d from 20 keV
13 truncated sequences
28
Source : G. Noguère PhD (2003)

## Slide 29: Prospects
From phenomenological to physics R-Matrix fission width amplitudes
How that? ≈ 2*Poverall barrier * Pf, class II
Extracted gf are still biased by Pf(J,K,P) (hopefully constant over the energy range under investigation (0-100 keV))
  Hill-Wheeler formula :
n+235U
s-waves: two possible resonances Jpi=3- and 4-
RM= 2 fission widths per Jpi
RM extended towards fission axis = 4 fission widths (labeled by Jπ K) per Jπ = 4 values of Pfoverall between 0.3 and 0.6

## Slide 30: Conclusion
Work done (presented):
Identification of class-II states in RRR assuming Lorentzian penetrability [Jπ dependence] (R-Matrix framework)
Identification of class-II states in URR assuming Lorentzian penetrability [Jπ independence] (average XS framework)
Work done (not presented):
[Neutron entrance channel] Identification of class-II states using centrifugal penetrability discrimination
[Fission exit channel] Statistics of class-II states and transition states supported by combinatory nuclear level density calculations (deformation dependent)

## Slide 31: Conclusion
Work done:
Actual representation of 2 class-II states in RRR assuming Lorentzian penetrability [Jπ dependence] (more physical framework)
Identification of 68 class-II states in URR assuming a Lorentzian penetrability [Jπ independence] (average XS framework) but some might be resolved class-I states
Study feedback:
First input in an evaluated file of class-II states information
Still some missing experimental data for 242Pu
Remain many RRR evaluated files using MLBW format (technologically obsolete)
How to fit the RM interferences when large experiment fission XS background is included in the observation ?
Need other studies to discriminate resolved class-I states in class-II states over the low energy URR
Parameters of these class-II states require special evaluated data file format to be supplied
31
Notes: Evaluated files GND

## Slide 32: Conclusion
Ongoing :
[Neutron exit channel] Study of the structure (at 1.1 MeV)
Study feedback:
First input in evaluated files of class-II states information
Still some missing experimental data for 242Pu
Still many RRR evaluated files in MLBW format (technologically obsolete)
How to fit the RM interferences when significant experiment fission XS background is observed ?

## Slide 33: Prospects
From phenomenological to physics R-Matrix fission width amplitudes
How that? ≈ 2*Poverall barrier * Pf, class II
Extracted gf are still biased by Pf(J,K,P) (hopefully constant over the energy range under investigation (0-100 keV))
  Hill-Wheeler formula :
n+235U
s-waves: two possible resonances Jpi=3- and 4-
RM= 2 fission widths per Jpi
RM extended towards fission axis = 4 fission widths (labeled by Jπ K) per Jπ = 4 values of Pfoverall between 0.3 and 0.6

## Slide 34: Thank you 
And thank to :
O. BOULAND
G. NOGUERE
M. DIAKAKI
L. MATHIEU M. AÏCHE

## Slide 35: Conclusions
n-ball & n-ball2 data have been analysed to complete the 238U level scheme
117 levels identified, including:
  60 already listed in ENSDF and 57 new
  92 found with both sets of data
268 g transitions identified , including:
  110 already listed in ENSDF and 158 new
  187 found with both sets of data
34 g transitions listed in ENSDF for which coincidences were impossible to check
53 g transitions listed in ENSDF for which no coincidences have been found
Most of contaminants have been analysed
Branching ratios have been extracted from the n-ball2 data set
Spin and parities (Jp) have been deduced from the Jps of the final levels and by completing bands

## Slide 36: n-Ball experiment
Detectors around the target 34 HPGe
    24 CLOVER
    10 HPGe
  BGO (scintillators) around each Ge
5 238U or 232Th disks
Neutron production target: H2 Pressure: 1.4 bar
3 data set
  238U, En=1,9 MeV – 9 days of data
  238U, En=3,3 MeV – 5 days of data
  232Th, En=1,9 MeV – 19 days of data

## Slide 37: Experiments goal
Neutron-rich fission fragments
Possibility of studying the structure of the target nucleus 238U
37

## Slide 38: Data used to start the analysis
Coincidences of g rays with a multiplicity of 2 or 3 selection mostly the g rays from the (n, n’g)
Disregard most of the g rays from fission (mean multiplicity of 5) and other parasitic g rays
Analysis of the n-Ball1 data with a multiplicity 2
Analysis of the n-Ball2 data with a multiplicity 2 to 4; Condition on energy sum ≤ 3300 keV
Courtesy of Jon Wilson
38

## Slide 39: Summary
PRC article accepted for publication
C. Chatel et al., Study of inelastic neutron scattering on 238U with γ ray coincidence spectroscopy
Repository with all the g-rays expected not coming from 238U published: C. Chatel et al., Gamma-ray contaminations identified in the study of inelastic neutron scattering on 238U, repository, DOI: 10.5281/zenodo.18199649 (2026)
238U + 68 nuclei analyzed
  40 fission fragments
  1792 g rays in coincidence
Not every g identified yet !!!
  756 g coming from fission fragments
  61 g in coincidence seen by fission partners
  21 potentially new g not coming from 238U
39

## Slide 40: Analysis of the n-Ball data - 238U level scheme - obtained results
40
103 levels identified
  Including 52 already listed in ENSDF
211 g identified
  Including 86 already listed in ENSDF
39 new g depopulating levels already known in ENSDF
51 new levels (not known in ENSDF)
86 new g (de)populating these new levels

## Slide 41: n-Ball2
41
Increased statistics (8 times)
Remove of some contamination by changing the beam dump and the target
  The main contamination of n-Ball (21Ne) has been deleted in n-Ball2
  3 new rays of contamination appear linked to the Au
Notes: new matrix with about 8 times more statistics in (n,n'). The background is also about half what it was in nu-Ball2. The contamination is less, particular from 21Ne (351 keV) etc.

## Slide 42: Contamination analysis
42
uBall
Conditions:
- multiplicity 2
uBall2
Conditions:
- multiplicity 2-4
- Etot ≤ 3300 keV
Notes: Raies or : 279 keV ; 547 keV ; 576 keV

## Slide 43
43
uBall
Conditions:
- multiplicity 2
uBall2
Conditions:
- multiplicity 2-4
- Etot ≤ 3300 keV
uBall2: Background subtraction spectrum

## Slide 44
44
uBall Gate on 635 keV
Conditions:
- multiplicity 2
uBall2 Gate on 635 keV
Conditions:
- multiplicity 2-4
Etot ≤ 3300 keV
Statistics: 8 times more!
Comparison n-Ball and n-Ball2– g 635 keV
Notes: new matrix with about 8 times more statistics in (n,n'). The background is also about half what it was in nu-Ball2. The contamination is less, particular from 21Ne (351 keV) etc.

## Slide 45: Total g-spectrum
Energy (keV)
Counts
45
Notes: matp_px obtenu avec MatProj sur Matp.m4b ; ici result_px

## Slide 46: Background profile
Energy (keV)
Counts
46
Notes: matp_bx obtenu avec MatProj sur Matp.m4b ; ici result_bx

## Slide 47: Background subtraction spectrum
Energy (keV)
Counts
47
Notes: Sp matp_px as -1 matp_bx

## Slide 48: 238U level scheme – n-Ball2
48
Inelastic scattering
Secondary reactions (Coulomb excitation, fusion, oxidation, etc.)
Fission

## Slide 49: 238U level scheme – n-Ball2
49
238U + 68 nuclei
  40 fission fragments
1524 parasitic gammas
  756 gammas coming from fission fragments
  61 gamma in coincidence seen by fission partners
  21 potentially new gammas
Not everything analysed
Not every main coincidences found

## Slide 50: 𝜈- Ball2 experiment
Fast neutron source (LICORNE)
High intensity 7Li beam: ~ 100 nA pulsed beam (prev. 10 nA)
H gas cell: 1.6 atm (prev. 1.4 atm)
238U target: ~106 g in chips (prev. 5 disks)
24 clovers + 20 FATIMA detectors
  Increase by 4 of the efficiency
2 runs
  July: 125 hours
  October: 214 hours
  Total: ~ 14.1 days
  Data clearer
  8 times more statistics
50

## Slide 51: Cibles 238U
51

## Slide 52
52

## Slide 53: Contamination Level Scheme
53

## Slide 54: Problems faced: statistics and contaminations
If we analyze the 384,5 keV g, we can see that:
The main coincidence is with 351 keV, which belongs to 21Ne and is the main contamination of the spectrum
The second main coincidences are the 2 g de-energizing the 731,93 keV level of the 238U but the statistics is quite low
  New level at 1116 keV (also found thanks to another g analysis) but a higher statistics would validate it
Main coincidence: 351 keV
Contamination
2nd main coincidences: 583 + 687 keV  238U
Statistics
Example: gate on 384.5 keV
54
Notes: Nouveau niveau à 1116 trouvé également par 808 en coïncidence avec 159 (niveau 307)

## Slide 55: Gate on contamination rays Example 209Bi - 896 keV
Contamination linked to 209Bi
Contamination linked to wide g (72Ge g of 894 keV ; 238U g of 899 keV)
Contamination linked to fortuitous coincidences
55