## Slide 1
An Alp-Sized Neutron Absorber:
Recent Discoveries and Measurements around 88Zr(,)
Dr. Will Flanagan
Research Scientist, University of Texas at Austin
Affiliate Research Assistant Professor, University of Dallas
will.flanagan@austin.utexas.edu

## Slide 2
My two main interests : 88Zr and 135Xe
135Xe
Largest thermal neutron capture cross section
Fission product
Neutron-Rich
Large neutron absorption cross section discovered in 1944
Radioactive (9.14 hours)
  88Zr
Second largest thermal neutron capture cross section
Not a fission product
Neutron-Poor
Large neutron absorption cross section discovered in 2019
Radioactive (83.4 days)
This is my talk today
Related to this, we are collecting FIPPS data for 6 stable xenon targets this summer
  Xenon has 9 stable isotopes
    129Xe(,)130Xe, 131Xe(,)132Xe, 136Xe(,)137Xe already well studied
      We will measure the other 6
      Preliminary 130Xe(,)131Xe measurement
      124Xe(,)125Xe to 134Xe(,)135Xe
An ultimate goal is 135Xe(,)136Xe (reactor heating, etc!)
  134Xe(,)135Xe is a main background

## Slide 3
88Zr(,) - Background
In 2019, 88Zr was discovered to have a thermal neutron absorption cross section of ~800,000 barns (measured) rather than 10 barns (“expected”).
  Larger than 157Gd, 10B, 6Li, 3He
  Smaller than 135Xe
88Zr is the only neutron absorber above 10,000 barns with even neutron number
Perhaps more surprising, many argue that thermal neutron cross sections are not able to be predicted!!!
S. Heinitz, U. Köster Nature Physics volume 15, 208–209 (2019)

## Slide 4
88Zr(,) - Background
135Xe
157Gd
113Cd
88Zr hidden on other side of mountain range. What else is hiding here?
(Fission products beta-decay to stability)

## Slide 5
88Zr is a neutron sponge – Who cares?
Nuclear physicists
  How are we wrong about predicting basic properties by 4 orders of magnitude?
High energy zirconium applications
  Accelerator and spallation sources
Is this massive cross section relating to new fundamental nuclear physics?
Does 88Zr ‘feel a tug’ towards the magic number of 50 neutrons (90Zr)?
Or was there simply an unexpected resonance at just the right (thermal) energy?
This is what turns out to be true

## Slide 6
88Zr(n,𝜸) – February 2024
2019 LLNL et. al. – thermal neutron capture 861,00069,000 barns
2021 LLNL et. al. – thermal neutron capture 804,00063,000 barns, resonance integral 2,530,000,000 barns
2023 LANL – thermal neutron capture 771,000,000 barns and resonance integral 15,210670 barns
  LANL DICER uses neutron ToF with transmission for energy-resolved measurement
  Resonance measured at 0.171 eV
    A. Stamatopoulos et al., “Origin of the enormous 88Zr neutron-capture cross section and quantifying its impact on applications,” Phys. Rev. Lett. 134, 112702 (2025)

## Slide 7
88Zr(n,𝜸) – February 2024
2019 LLNL et. al. – thermal neutron capture 861,00069,000 barns
2021 LLNL et. al. – thermal neutron capture 804,00063,000 barns, resonance integral 2,530,000,000 barns
2023 LANL – thermal neutron capture 771,000,000 barns and resonance integral 15,210670 barns
  LANL DICER uses neutron ToF with transmission for energy-resolved measurement
  Resonance measured at 0.171 eV
    A. Stamatopoulos et al., “Origin of the enormous 88Zr neutron-capture cross section and quantifying its impact on applications,” Phys. Rev. Lett. 134, 112702 (2025)

## Slide 8
88Zr(,) – Measurement Challenges
88Zr Produced from protons on yttrium at LANL IPF.
  89Y(,2)88Zr
88Zr is radioactive with an 83.4 day half life.
Decays to 88Y with a 106.6 day half life

## Slide 9
88Zr(,) – Measurement Challenges
88Y buildup creates a major background
88Zr electron capture produces 393 keV gammas (97% branching ratio)
But 88Y electron capture produces 898 keV (93%) and 1.836 MeV (99%) gamma rays.
88Zr arrives from LANL in 2M HCl
Developed 88Zr/88Y chemical separation
88Zr metal cation complexes with (HDEHP)2 and dissolves in the organic layer
  Then digest dodecane with oxalic acid, nitric acid, peroxide
For later ILL FIPPS run, additional water “washes” to rid 35Cl before digesting organic.

## Slide 10
88Zr(,) – Isomeric Yield Ratio
How often is compound nucleus “trapped” in metastable state after capture?
  Isomeric Yield Ratio
  89mZr 588 keV above ground state 89gZr
  88Zr(n,)89gZr - 9.3 MeV of prompt gammas
  88Zr(n,)89mZr – 8.7 MeV of prompt gammas
10-minute irradiation at UT NETL (TRIGA) reactor
  Reactor core 1013 n/cm2/s
Pneumatic transfer to HPGe counting room
Data collection begins 3 minutes after irradiation

## Slide 11
88Zr(,)89m/89gZr – HPGe Spectra
Prominent lines for 89mZr:
  588 keV (IT) and 1507 keV (in conjunction with emission)
  Confirmed previous measurements of 89mZr branching ratios
    D. Van Patter and S. Shafroth, Decay of 78.4 h 89Zr and 4.18 min 89mZr, Nucl. Phys. 50, 113 (1964)
Prominent line for 89gZr:
  393 keV (EC to 89Y)
Other prominent lines:
  511 keV
  1273 keV (29Al)
  1779 keV (28Al)
    88Zr evaporated on Kapton tape substrate

## Slide 12
88Zr(,) – Isomeric Yield Ratio
Fit ratio of most prominent 89mZr and 89gZr lines over time.
Shape is predominantly 89mZr 4.2min half life over (fairly constant, 78.4hr) 89gZr abundance, except that 89mZr decays also feed 89gZr.
Vary isomeric yield ratio as well as 7 sources of systematic uncertainty
Best fit at minimum
  7 penalty terms associated with systematics
68% C.L. at increase of 1

## Slide 13
88Zr(,) – Isomeric Yield Ratio
Fit ratio of most prominent 89mZr and 89gZr lines over time.
Shape is predominantly 89mZr 4.2min half life over (fairly constant, 78.4hr) 89gZr abundance, except that 89mZr decays also feed 89gZr.
Vary isomeric yield ratio as well as 7 sources of systematic uncertainty
Best fit at minimum
  7 penalty terms associated with systematics
68% C.L. at increase of 1
89mZr is populated 74.90.6% of the time
Published in Phys. Rev. C last month

## Slide 14
Our isomeric yield ratio: 74.9±0.6%.
TALYS with 89Zr energy levels given by RIPL-3, predicts 89%.
2019 discovery paper (Shusterman et al) assumed 88Zr(n,) always produced 89mZr
And they measured the 88Zr(n,) cross section by accounting for the amount of 88Zr destroyed and 89gZr produced.
  They assumed 6% of 88Zr(n,) neutron captures didn’t produce 89gZr due to 89mZr’s 6% decay to 89Y
  But we show that 25.1% of 88Zr(n,) produces 89gZr directly
  And only 74.9% of 88Zr(n,) produces 89mZr
    So only 6% 74.9% = 4.5% of reactions create 89Y instead of 89gZr
1.5% difference in amount of 89Y predicted.
Relevance to Other Measurements
74.9%
25.1%

## Slide 15
Moving Forward - Neutron Capture
Neutron capture creates compound nucleus
  Excess energy creates prompt gamma rays

## Slide 16
Neutron Time of Flight at CERN
LINAC4 H- 160 MeV ; Booster H+ 2 GeV ; Proton Synchrotron H+ 25 GeV
7ns proton bunch width, lead spallation target

## Slide 17
Neutron Time of Flight at CERN
Experimental Area 2 (EAR2) utilized due to higher instantaneous flux, fast segmented Total Energy Detectors (C6D6 sTEDs), and “almost dead-time free” DAQ.
Target upgrade

## Slide 18
Neutron Time of Flight at CERN
Evaporation of salt not uniform!
  Beam interception factor
Neutron radiograph from NEUTRA at Paul Scherrer Institute.
  March 2024 (test) deposition
  July 2024 image
Lesson learned for (main) August 2024 sample!
More uniform deposition at PSI

## Slide 19
Minimize Detector Rate
Obtained 1mCi 88Zr source from LANL IPF for March test exposure at CERN n_TOF
  Allowed us to test shipping logistics to Europe
Obtained 30mCi 88Zr source from LANL IPF for August-September beam time.
  5 AUG 24 LANL separation
  12 AUG 24 receipt at PSI
  16 AUG 24 begin irradiation at CERN
Lead shielding to attenuate 85% of 88Zr activity while maintaining roughly half of prompt gammas.

## Slide 20
Shielding Validation (March 2024)

## Slide 21
Detector Rates (August 2024)
Maintained a detector rate below 1 MHz to assure detector performance
  Continuous calibrations with 88Y

## Slide 22
88Zr – Deposited Energy (Gammas)
Compton shoulders:
88Zr 393 keV (97%)
88Y 898 keV (94%)
88Y 1.836 MeV (99%)
88Y 2.734 MeV (0.6%)
88Y 3.218 MeV (0.007%)

## Slide 23
88Zr – Background Subtraction
Require 3.5 MeV of energy to be deposited in scintillators
  To eliminate 88Zr and 88Y EC gammas

## Slide 24
88Zr – Resonance Found
We confirm the resonance suggested by LANL DICER (transmission) at 0.17 eV!
  Single Level Breit Wigner fit parameters within 1
But our normalization is difficult…
  We don’t know our gamma cascades (and efficiencies of gamma energy cuts)
Normalize based on LLNL thermal measurement
Transmission (LANL DICER)
Capture (CERN n_TOF)

## Slide 25
88Zr – ILL FIPPS
Next steps - prompt gamma cascades at ILL FIPPS (thermal, 108 neutrons/s/cm2, 64 HPGe)
  FIPPS has successful record with radioactive samples (2MBq calcium-41 and 2GBq nickel-63, for example)
  Two Campaigns in Fall 2025

## Slide 26
88Zr – ILL FIPPS
Promising results so far!
  PRELIMINARY!!!
Red denotes new candidate states/gammas
Black denotes previously known.
Credit: C. Michelagnoli

## Slide 27
88Zr – Conclusions
The 88Zr(n,) thermal cross section is anomalously large because of a sub-eV resonance.
  We confirm the (transmission-based) DICER 0.17 eV resonance.
CERN INTC approval to measurement was less than 1 year.
  Rapid progress is possible when partners like LANL, PSI, and CERN work together!
And infusion of ILL FIPPS data helps to complete the story!
  Improved understanding of prompt gamma energy deposited in n_TOF scintillators
    FIPPS helps to optimize n_TOF analysis
  Relative Absolute cross section at n_TOF
Many thanks to brilliant collaborators and students!
UT NETL reactor, radiochemistry – Don Nolting, Joseph Lapka, Bill Charlton, Tracy Tipping, Rodrigo Viveros
89mZr – Isaac Kelly (undergraduate PhD student at Notre Dame), Jacob Moldenhauer
CERN n_TOF – Genevieve Alpar (undergraduate Master at AFIT), Albert Parmenter (undergraduate), Beth Jacoby (undergraduate), Michi Bacak, Javi Balibrea, Claudia Lederer-Woods, Jorge Lerendegui-Marco, Emilio Maugeri, Alberto Mengoni
ILL FIPPS – Caterina Michelagnoli, Marek Stryjczyk and many from n_TOF including Matt Birch, Toby Wright, Fran Garcia-Infantes, Javi Balibrea, Jorge Lerendegui-Marco, Michi Bacak + Andrew Rosen (undergraduate) and Tanner Gordon